## Slide 1: XENONnT: Towards Solar pp Level Background in the Electron-Recoil Detection Channel
Ying-Ting Lin, on behalf of the XENON Collaboration University of Münster, Institute for Nuclear Physics, Germany IDM 2026 Zaragoza, Spain, 03.06.2026
LowRad
NASA/SDO

## Slide 2
Gran Sasso National Laboratory (LNGS), Italy
Collaboration Meeting 2025 at LNGS
The XENON Collaboration
200+ members
31 institutes
12 countries

## Slide 3
Going underground (3.6 km water equivalent)
Active muon and neutron vetoes / extra shielding
Detector material: cleaning and screening
Accurate position reconstruction: fiducial volume (FV)
  S1: prompt scintillation, light signal
  S2: drift electrons, charge signal
GeMPI, MPIK
Auto-Ema, MPIK
5.9 tonne target LXe mass
Background Reduction Prerequisites for Rare Event Searches
3
Ying-Ting Lin, ylin3@uni-muenster.de
  Gd-Loaded Neutron Veto: Emanuele Angelino, Jun 4th, 15:15, Pedro Cerbuna
Notes: As a prerequisite to greatly reduce the background from the start, for the XENONnT experiment, it is located underground in the Gran Sasso National Lab, with active muon and neutron veto surrounding the detector in center here
We must protect our signal at all cost from all the other background noises that can enter into the detector. In the XENONnT, we place the detector deep in the mountain at the Gran Sasso national lab with 1.5km of rock overburden and put up a muon veto to shield from the cosmogenic background and an additional neutron veto to reduce the background from fast neutron emitted by the rocks in the mountains
1.5km of rock, 3.6 km water-equivalent
Radiogenic neutrons emitted by mountain material
For the detector, the material selection is an important effort, including screening of radioactive emanation with specifically developed instruments such as GeMPI and Auto-Ema. The detector is a dual phase TPC with S1 light signal and S2 drift change signal, available for fiducial volume selection. And to improve the purity of the the center most clean xenon area
https://www.mpi-hd.mpg.de/lin/research_LLL.en.html
automated emanation system (Auto-Ema), https://www.mpi-hd.mpg.de/mpi/en/public-relations/news/news-item/extreme-purity-for-the-hunt-for-dark-matter
Also leak tightness to prevent Kr from getting in, especially during the pump down stage
Recent development in the Galinalium-loaded neutron veto

## Slide 4
ER/NR Discrimination
S2/S1 ratio is different for Electronic Recoils (ER) and Nuclear Recoils (NR), resulting in two separate bands
ER
NR
ER (Electronic Recoils):
electron, photon, neutrino, (axions…)
NR (Nuclear Recoils):
neutron, CEvNS, (WIMPs…)
XENON Collab., Phys. Rev. Lett. 131, 041003 (2023)
XENON Collab., Phys. Rev. Lett. 131, 041003 (2023)
4
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: Lindhard quenching
In calibration data versus in the science data, the majority of the remaining background events are ER events

## Slide 5
Dark Matter and New Physics Searches in the ER Channel
Region of Interest (ROI): ER channel in [1, 140] keV range
5
Ying-Ting Lin, ylin3@uni-muenster.de
Prediction for XENONnT Science Run 1 (SR1)
Solar
Axion
Peak-like Signals:
Dark Photon
Axion-like particles
Updated from
XENON Collab., Phys. Rev. D 102, 072004 (2020)
Neutrino Magnetic Moment
Notes: * Beyond the Standard Model

## Slide 6
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/220Rn
85Kr
Xenon Isotopes:
136Xe/124Xe
133Xe/125I
Other backgrounds:
Materials
3H-like
83mKr
Accidentals
Neutrinos:
Solar
6
Ying-Ting Lin, ylin3@uni-muenster.de
ROI: ER channel in [1, 140] keV range
Notes: Mention it;s

## Slide 7
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/220Rn: decay daughters of the material; dominant ER background
85Kr
Xenon Isotopes:
136Xe/124Xe
133Xe/125I
Other backgrounds:
Materials
3H-like
83mKr
Accidentals
Neutrinos:
Solar
ROI: ER channel in [1, 140] keV range
7
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: - Detector material

## Slide 8
222Rn/220Rn: Removal & Monitor
ER background comes from 214Pb beta decay
Continue radon removal with ~ 72kg/h high flow
Alphas from decay chain to constrain 214Pb
Reduced 222Rn activity down to 1 Bq/kg level! XENON Collab., Phys. Rev. X 15, 031079 (2025)
S. Bruenner, D. Cichon, G. Eurin, P. Herrero Gómez, F. Jörg, T. Marrodán Undagoitia, H. Simgen, N. Rupp, Eur. Phys. J. C 81, 343 (2021)
Notes: - In other word, we can use XENONnT data to set such constraint
Pb210 lifetime too long so settle on the wall
The focus will be on the Rn222 analysis, but as accuracy improves, so will be contribution from Rn220
Explain plate-out ratio

## Slide 9
222Rn: Estimation
Decay chain one-to-one up to plate-out
Utilizing the 222Rn calibration sample
Precise estimation of 214Pb/222Rn ratio
Total uncertainty for 214Pb rate: < 5%
F. Jörg, G. Eurin, H. Simgen, Appl. Radiat. Isot. 194, 110666 (2023)
222Rn Sample
9
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: - Event rate goes up by 2 orders of magnitude
- Remove the first few data point as not at equilibrium
- RAD at work in removing Rn222

## Slide 10
220Rn: Estimation
ER background comes from 212Pb beta decay
Tracing alphas from 220Rn calibration (instant injections) by difference equations with decay constants and plate-out ratios
Use asymptotic equilibrium to predict 212Pb/( 212Bi, 212Po) ratios
S. Bruenner, D. Cichon, G. Eurin, P. Herrero Gómez, F. Jörg, T. Marrodán Undagoitia, H. Simgen, N. Rupp, Eur. Phys. J. C 81, 343 (2021)
10
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: Cannot use the previous method because the alpha before has such short lifetime
Because of the model dep, we apply high uncertainty
Equilibrium assuming constant injection
18.6% and 12.2% uncertainty

## Slide 11
Radon Calibration Science Search
Determination of 212Bi beta spectrum shape
XENON Collab., Phys. Rev. C 113, 044303 (2026)
Determination of 214Pb/212Pb beta decay branching ratio to ground/excited states
11
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: - To be published on arXiv soon

## Slide 12
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/ 220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in the residual air in xenon inventory or after pump-down
Xenon Isotopes:
136Xe/124Xe
133Xe/125I
Other backgrounds:
Materials
3H-like
83mKr
Accidentals
Neutrinos:
Solar
ROI: ER channel in [1, 140] keV range
12
Ying-Ting Lin, ylin3@uni-muenster.de

## Slide 13
5.5m
XENON Collab., Prog. Theor. Exp. Phys., 053H01 (2022)
Online krypton distillation column
Measurements with Rare Gas Mass Spectrometer (RGMS) using chromatographic separation:
Capable of reduction to sub-100 ppq level natKr/Xe ppq = parts per quadrillion = 10-15
XENON1T
85Kr: Krypton Distillation and RGMS Measurements
13
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: - Using chi2 error function to incorporate the data point error bars

## Slide 14
85Kr: RGMS Results for Science Run 1 (SR1)
SR1a has unintended gas introduction
Two models: natKr outgassing versus constant over time
85Kr/natKr abundance time evolution considered
M. Guida, Y.-T. Lin, and H. Simgen, Eur. Phys. J. C, 85, 14262 (2025)
14
Ying-Ting Lin, ylin3@uni-muenster.de

## Slide 15
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/ 220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in the residual air in xenon inventory or after pump-down
Xenon Isotopes:
136Xe/124Xe: natural xenon isotopes
133Xe/125I: activation from neutron calibration
Other backgrounds:
Materials
3H-like
83mKr
Accidentals
Neutrinos:
Solar
ROI: ER channel in [1, 140] keV range
15
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: Since we are using a lot of xenon target

## Slide 16
Xenon Isotopes
136Xe: abundance estimated using residual gas analyzer
124Xe: left free as a handle to the fit
133Xe: from decay models since calibration and estimated activation rate outside detector
125I: from decay models with 125Xe
XENON Collab., Nature volume 568, pages 532–535 (2019)
ROI: ER channel in [1, 140] keV range
16
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: Mention about the shape

## Slide 17
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/ 220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in the residual air in xenon inventory or after pump-down
Xenon Isotopes:
136Xe/124Xe: natural xenon isotopes
133Xe/125I: activation from neutron calibration
Other backgrounds:
Materials: gamma with Compton scattering
3H-like
83mKr
Accidentals
Neutrinos:
Solar
17
Ying-Ting Lin, ylin3@uni-muenster.de
ROI: ER channel in [1, 140] keV range
Notes: - Flat due to Compton scattering

## Slide 18
Materials: Full-chain Simulation
Full-chain GEANT4 with waveform simulation (WFsim) using screening values
Reconstructing both single-site and multi-site events
Notes: - Low energy more susceptible to detector effects and event selections

## Slide 19
Materials: Estimation
Investigating the data 2 cm outside the FV
Using the rate comparison between the simulation and data as systematic uncertainty
19
Notes: * Dominated by material event, while less spectrum alteration
* Subtracting the central most events to isolate material background spectrum

## Slide 20
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/ 220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in the residual air in xenon inventory or after pump-down
Xenon Isotopes:
136Xe/124Xe: natural xenon isotopes
133Xe/125I: activation from neutron calibration
Other backgrounds:
Materials: gamma with Compton scattering
3H-like: potentially from operation
83mKr: residual from calibration
Accidentals: accidental coincidences
Neutrinos:
Solar
ROI: ER channel in [1, 140] keV range
20
Ying-Ting Lin, ylin3@uni-muenster.de
  WIMP: Maxime Pierre, Jun 2nd, 12:10, Aula Magna
  CENS: Giovanni Volta, Jun 2nd, 11:30, Pedro Cerbuna

## Slide 21
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/ 220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in the residual air in xenon inventory or after pump-down
Xenon Isotopes:
136Xe/124Xe: natural xenon isotopes
133Xe/125I: activation from neutron calibration
Other backgrounds:
Materials: gamma with Compton scattering
3H-like: potentially from operation
83mKr: residual from calibration
Accidentals: accidental coincidences
Neutrinos:
Solar : non-shieldable, dominate by pp neutrinos in low-energy ROI
ROI: ER channel in [1, 140] keV range
21
Ying-Ting Lin, ylin3@uni-muenster.de

## Slide 22
Low ER Region Search: pp-chain Solar Neutrino
The low-energy region of ER channel will be dominated by the elastic electron-neutrino scattering of solar pp neutrinos
The cross-section models in xenon:
  Free Electron Approximation (FEA) with stepping correction
  Relativistic Random Phase Approximation (RRPA)
J. -W. Chenetal, et al., Phy. Lett. B. 774, 656–661 (2017)
BOREXINO Collaboration, Nature 562, 505–510 (2018)
22
Ying-Ting Lin, ylin3@uni-muenster.de
ν
e-
e-
ν
W
Notes: - The cross-section is much smaller, but signal response much larger as compared to CEvEN

## Slide 23
Backgrounds in ER Channel
ROI: ER channel in [1, 140] keV range
23
Ying-Ting Lin, ylin3@uni-muenster.de
BOREXINO (280 tonne)
GALLEX/GNO SAGE (30-60 tonne)
XENONnT (5.9 tonne)
XENONnT ER channel background now reduced to solar pp level
Notes: Background reduced to solar-pp level

## Slide 24
Fiducial Volume Estimation
 | Lower (%) | Upper (%)
FV | 9.7 | 10.0
Uncertainty of Solar pp Measurement
Field distortion correction
Charge incentive area simulation
FV optimized using simulated material background based on signal to background figure of merit
FV value: overall 3% uncertainty from field map
Event position resolution uncertainty is negligible
24
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: In order to measure the solar pp flux, we need to do more then rate measurement, but incorporate all the error budgets
Charge insensitive area by PyCOMes

## Slide 25
Uncertainty Budget for Solar pp Measurement (SR0+SR1)
 | Lower (%) | Upper (%)
FV | 9.7 | 10.0
Efficiency | 7.1 | 7.3
214Pb rate | 4.3 | 4.1
214Pb spectrum | 1.1 | 1.1
136Xe spectrum | 1.0 | 1.0
Energy Bias | 2.8 | 4.0
Energy Resolution | 1.2 | 1.4
Total Post-Inference Systematics | 13 | 14
Uncertainty of Solar pp Measurement
25
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: Charge insensitive area by PyCOMes

## Slide 26
Achieved the lowest ER background in direct dark matter experiments
Precise determinations of the remaining ER background has been established along with comprehensive systematic budget
Measurement of solar pp is within reach, opening to future dark matter searches in ER channel
Summary and Prospect
NASA/SDO
26
Ying-Ting Lin, ylin3@uni-muenster.de
Notes: - With SR0/SR1 data

## Slide 27
Aiming for sub-% accuracy in solar pp flux measurement
  222Rn: 0.1 Bq/kg
  natKr/Xe: 30 ppq
    < 10% constraint to 214Pb
    < 10% constraint to 85Kr
The Next Generation Experiment
XENON Collab., Phys. Rev. X 15, 031079 (2025)
x6
x3
LowRad
XLZD Collab., The XLZD Design Book, Eur. Phys. J. C 85, 1192 (2025)
DARWIN Collab., Eur. Phys. J. C 80, 1133 (2020)
Notes: What we have done has shown such precision measurement for solar pp flux is completely possible

## Slide 28: Backup Slides

## Slide 29
Liquid Xenon Target
Credit Plot: L. Hötzsch
scintillation yield ≃ 46 γ/keVee
ionization yield ≃ 64 e-/keVee

## Slide 30: Electron Drift and Extraction
Credit Plot: T. Marrodán Undagoitia
30
Notes: - Threshold at 2kV/cm
- Amplification of 20-30PE per electron

## Slide 31
Data from Air Liquide Encyclopedia
High mass number: high density (3 g/cm3), high nuclear interaction cross-section
Liquid Xenon (LXe) Rare Event Detection
T. Marrodán Undagoitia, L. Rauch, J. Phys. G: Nucl. Part. Phys. 43 013001 (2016)
Homogeneity: liquid target under cryogenic temperature
Noble gas: can achieve high purity
Low intrinsic background
Vacuum Ultra-violet (VUV) scintillation: high light/charge yield
Time projection chamber (TPC) allow 3D position reconstruction
Ying-Ting Lin ylin3@uni-muenster.de

## Slide 32: Electronegative Impurity in LXe
e-
e-
e-
e-
e-
e-
e-
e-
e-
O2
O2
e-
e-
O2
e-
low e- loss
high e- loss
H2O: resides on metal surfaces
  Light attenuation at scintillation wavelength
  Uniform reduction of S1 signal
O2: resides within porous material such as PTFE
  High electron attenuation; capturing drift electrons
  Depth dependent loss of S2 signal
  Quantified by electron drift lifetime: : O2 concentration, : rate constant
  Number of S2 electrons lost at drift time :
Notes: To ensure the signal quality, the first type of impurity we would like to remove is this
23V/cm
Maximum drift time of 2.2ms
Height of 140cm
H2O:
- substantial light absorption cross-section at the scintillation wavelength of LXe (175 nm)
- H. Keller-Rudek, G. K. Moortgat, R. Sander, and R. SÅNorensen. The MPI-Mainz UV/VIS Spectral Atlas of Gaseous Molecules of Atmospheric Interest. Earth Sys1766
tem Science Data, 5(2):365–373, 2013.
- A. Baldini et al. Absorption of scintillation light in a 100l liquid xenon γ-ray detector and expected detector performance. Nucl. Instrum. Meth. A, 545(3):753–764, 2005.
O2:
- https://pubs.acs.org/doi/10.1021/j100564a006

## Slide 33
ER Calibration
: work function
/: photon/electron detection efficiency: number of observed PMT photoelectrons (PE) per scintillation photon/ionization electron produced
33
Notes: As low as Argon shells:
- K-shell, 2.8224 keV, 90.21%
- L-shell, 0.2702 keV, 8.72%
- M-shell, 0.0175 keV, 1.06%

## Slide 34: XENON1T/nT Gas Purification
impurity at equilibrium
total impurity source inflow
flow turnaround time from TPC
purifier efficiency
total LXe
E. Aprile et al. (XENON Collab.), Eur. Phys. J. C. 84, 784 (2024)
Hot Getter
E. Brown et al., Eur. Phys. J. C. 78, 604 (2018)
Mag-Pump
General purification performance equation:
Hot getter purifiers
Magnetic GXe pumps (mag-pumps): 22-36 kg/h 60-100 slpm
Achieved electron drift lifetime: 650
Notes: Mag pump developed together with the nEXO group, already goes down to hundred of microseconds
Turn-around time of about 7 days for 3.2 tonnes
Read out from pre-amp on cathode grid
Electron cloud from photo-electric effect on titanian/gold coated Al disk

## Slide 35: XENONnT Liquid Purification
Magnetically coupled cryogenic rotor pumps: 180-720 kg/h 1-4 LPM
Purifiers:
  copper catalyst on high-surface-area alumina (Q5): high , higher radon emanation
  sintered pellets of non-evaporable getter alloy (St707): lower , low radon emanation
35
Barber-Nichols
Notes: 1 LPM ~ 500 slpm ~ 180 kg/h
100 slpm ~ 36kg/h

## Slide 36: XENONnT Liquid Purification Performance
With Q5, achieved 5 ms electron drift lifetime in 5 days
In science run with St707, kept at 15 ms electron drift lifetime: ~90% full-drift electrons survive
G. Plante et al, Eur. Phys. J. C 82, 860 (2022)
Xeclipse Purity Monitor
Q5 Performance
Electron Drift Lifetime [s]
St707 Science Run Performance
Electron Drift Lifetime [ms]
Notes: Turn-around time of 0.9 days for entire 8.6 tonnes
Read out from pre-amp on cathode grid
Electron cloud from photo-electric effect on titanian/gold coated Al disk

## Slide 37: Noble Gas Cryogenic Distillation
PhD thesis
M. Murra (2019)
222Rn
85Kr
Relative volatility as vapor pressure ratio:
85Kr: 10.5 (-100C)
  Enriched at the top
  Remove through off-gas
222Rn: 0.1 (-100C)
  Enriched at the bottom
  Trapped in reboiler to decay
Data from CRC Handbook of Chemistry and Physics 95th Edition
10.7yr
26.8min
Notes: - Talk about condenser, reboiler
Packing material required to facilate the separation between gas and liquid concentration

## Slide 38: XENONnT Krypton Distillation
E. Aprile et al. (XENON Collab.), Eur. Phys. J. C. 77, 275 (2017)
5.5 m
38
Distillation mode: Offline and online
Feeding flow:
  3 kg/h 8.3 slpm
  Achieved: 6.5 kg/h 18 slpm
Separation factor:
  104-105
  Achieved:
Xe recovery: 99%

## Slide 39: XENONnT Radon Removal
E. Aprile et al. (XENON Collab.), Eur. Phys. J. C. 82, 1108 (2022)
39
Distillation mode: Continuous online
Feeding flow (radon-free mag-pumps): targeting 72kg/h 200 slpm (~15% of LXe flow)
Separation factor: >156
XENON Collaboration, Phys. Rev. X 15, 031079 (2025)
Xe recovery: 100%
Reboiler heat exchanger (HE)
Mag-pump compressor acts similar to a heat pump via another HE
Improve power consumption for cooling by a factor of 3!
Notes: * While Kr is concentrated in the gaseous form, radon stays well inside LXe, most effective with LXe inlet: Type1, Type2 source
* Factor of 3 reduction in power required, drastically reduce nitrogen consumption

## Slide 40
Alpha Analysis: S1S2 versus S1-Only Peak Comparison
S1S2 Mode
S1-only Mode
Notes: Should be in principle the same background data set

## Slide 41
ER Region Analysis: XENON1T BSM Limits
41
Phys. Rev. Lett. 129, 161805 (2022)
Neutrino Magnetic Moment
Axion-like Particle
Dark Photon
Solar
Axion
Notes: - Also blind analysis

## Slide 42
Materials: Estimation
Compton scattering of from trace radioactive material in detector surface
Full-chain simulation using Geant4 and waveform simulation (WFsim) with screening values as input
Side-band data from 2 cm outside the FV
42
Notes: * Dominated by material event, while less spectrum alteration
Subtracting the central most events to isolate material background spectrum
Rate comparison between the simulation and data as systematic uncertainty

## Slide 43
Backgrounds in ER Channel
Noble gas backgrounds:
222Rn/220Rn: decay daughters of the material; dominant ER background
85Kr: from natKr in Xe in the xenon inventory
Xenon Isotopes:
136Xe/124Xe: natural xenon isotopes
133Xe/125I: activation from neutron calibration
Other backgrounds:
Materials: gamma with Compton scattering
3H-like: potentially from operation
83mKr: residual from calibration
Accidentals: accidental coincidences
Neutrinos:
Solar : non-shieldable, dominate by pp neutrinos in low-energy ROI
ROI: ER channel in [1, 140] keV range
43
Ying-Ting Lin, ylin3@uni-muenster.de
(log)
Notes: Background reduced to solar-pp level

## Slide 44
Other Backgrounds
3H-like: potentially introduced in SR1a along with natKr
83mKr: residual from 83mKr calibration, removing 24h of science data after injection
Accidentals: accidental coincidences are negligible for science data, but important during 222Rn/220Rn calibrations due to pileups
Critical for searches in other channels:
  WIMP: Maxime Pierre, Jun 2nd, 12:10, Aula Magna
  CENS: Giovanni Volta, Jun 2nd, 11:30, Pedro Cerbuna
ROI: ER channel in [1, 140] keV range
44
Ying-Ting Lin, ylin3@uni-muenster.de

## Slide 45: LowRAD Project Goals
XENON Collaboration, Phys. Rev. X 15, 031079 (2025)
Low Radon and Low Internal Radioactivity (LowRad) ERC Advanced Grant
High flow radon removal with factor of 10 combined improvement in radon reduction to: 0.1 /kg of xenon
Lossless online krypton removal at: 30 x 10-15 (natKr/Xe)
All-in-one purification & distillation system
R&D for novel purification methods
Advancing analysis method for physics search
LowRad

## Slide 46
Compact Solar Neutrino Detector
Super-Kamiokande (50k ton)
SNO+ (780 ton)
BOREXINO (280 ton)
XENONnT (5.9 ton)
KamLAND (1k ton)
GELLAX/GNO SAGE (30-60 ton)
46
DEAP-3600 (3.6 ton)
Notes: Not only does xenon has sensitivity in B8 from CEvNS
Only BOREXINO has live signal for solar pp